## Slide 1
10Bit Processor
Fall 2023, South Dakota State University
BitBlaster
John Akujobi - Aman Ayelew - Sukhmanjeetsingh LNU
CSC 244 – Digital Logic

## Slide 2
Introduction
BitBlaster is a 10 bit processor designed and implemented on the DE-10 Lite
Features:
Input: Uses binary switches to input data
Performs bitwise manipulations

## Slide 3
Used for IoT devices like calculating microwave cook times based on variables like weight
Entry Level Embedded Systems
01
Developing low-complexity algorithms before implementing on advanced processors
Prototype Development
02
Helps students understand basic processor operations and digital logic design
Educational Environment
03
Applications that need a unique set of computational operations
Customizable Computing
04
Real-World Applications

## Slide 4
Theory

## Slide 5
System Architecture
Register File
Output Logic
Multistage ALU
Controller
Counter
Instruction Register
Input
Logic
Saves the instruction
Gets & processes instructions from external input
Sets up timesteps
Displays the output
Saves data in 4 registers
Controls the processor
Processes Arithmetic operations
Shared BUS: Transfers data between components
SDRAM
Stores data
Connects all modules
Top Level

## Slide 6
Top Level View

## Slide 7
Instruction Sheet
Function | Opcode | Details | Procedure | T0=00 | T1=01 | T2=10 | T3=11
LOAD ld Rx |  | Load data into Rx from slide switches | Rx ← Data | Extrn = 1 enIR = 1 | enRin = 1 Rin = Rx |  | 
COPY cp Rx, Ry |  | Copy value from Ry to Rx | Rx ← [Ry] |  | Rout = Ry enRout = 1 Rin = Rx Clr = 1 |  | 
ADDI Addi Rx, 6’bIIIIII |  | Add immediate values to RX |  |  |  |  | 
SUBI subi Rx, 6’bIIIIII |  | Subtracts immediate value from RX |  |  |  |  | 
LDR ldr Rx, *Ry | 00_XX_YY_1100 | Load data stored in RAM (at the 10-bit address stored in Ry) to register Rx |  |  |  |  | 
STR Str *Rx, Ry | 00_XX_YY_1101 | Store the data from Ry into RAM at the 10-bit address stored in Rx |  |  |  |  | 

## Slide 8
Operations

## Slide 9
Keys & Meanings
Key | Meaning and Details
Function | The name of the operation being carried out
Rx | Rx register Rx = INST [7:6] Contains the result at the end of most of the operations
Rx | Ry register Ry = INST [5:4]
ENR | Enables the bus to read from the register Enable for Q0
WNR | Enables the bus to write to the register
INST | IIIIII, UUU, enIR, Rout, Rin
Key | Meaning and Details
INST | 10 bit instruction gotten from instruction register
Rx | Rx register Rx = INST [7:6] Contains the result at the end of most of the operations
Rx | Ry register Ry = INST [5:4]
ENR | Enables the bus to read from the register Enable for Q0
WNR | Enables the bus to write to the register
INST | IIIIII, UUU, enIR, Rout, Rin

## Slide 10
Memory Movement
00
01
T00: 0th Timestep
- Enable Extern: get the instruction from the switches into the BUS
- Enable IR: store instruction in Instruction Register
T 01: 1st Timestep
- Enable Extern: writes the data value to the bus
- Rin = Rx: Prep the Rx register to read from the bus
- Enable Rin: Lets the register file read data from the bus
- CLR = 1: End the operation using the clear signal and reset the counter.
Load
LOAD, COPY

## Slide 11
Memory Movement
Function | Mnemonic | Opcode | Details | Procedure | T0=00 | T1=01
LOAD | ld Rx | 00_XX_UU_0000 | Load data into Rx from slide switches | Rx ← Data | Extrn = 1 enIR = 1 | enRin = 1 Rin = Rx
COPY | cp Rx, Ry | 00_XX_YY_0001 | Copy value from Ry to Rx | Rx ← [Ry] |  | Rout = Ry enRout = 1 Rin = Rx Clr = 1

## Slide 12
Arithmetic
T00
T01
T 11
T 10
T00: 0th
- Enable Extern: get the instruction from the switches into the BUS
- Enable IR: store instruction in Instruction Register
T01: 1st
- Rout = Rx: Prep the Rx register to write to bus.
- Enable enRout: - Let register file write data from Rx to bus
- Enable Ain: Let the A register save the value from the bus
T 11: 3rd
Activate Clr to send the done signal.
The BUS currently holds the result from Gout."
T 10: 2nd
-Stop SD register reading (EN_AddressRegRead = 0).
-Enable RAM to read from BUS
(ENRam = 1).
-Prepare Ry for writing by setting Rout to Ry, then enable Rout for the write operation, allowing the register to write to the bus."
ADD, SUB, XOR, OR, AND
ADD Rx, Ry
00_XX_YY_0010

## Slide 13
Arithmetic
Function | Opcode | Details | Procedure | T0=00 | T1=01 | T2=10 | T3=11
LOAD ld Rx |  | Load data into Rx from slide switches | Rx ← Data | Extrn = 1 enIR = 1 | enRin = 1 Rin = Rx |  | 
COPY cp Rx, Ry |  | Copy value from Ry to Rx | Rx ← [Ry] |  | Rout = Ry enRout = 1 Rin = Rx Clr = 1 |  | 
ADDI Addi Rx, 6’bIIIIII |  | Add immediate values to RX |  |  |  |  | 
SUBI subi Rx, 6’bIIIIII |  | Subtracts immediate value from RX |  |  |  |  | 
LDR ldr Rx, *Ry | 00_XX_YY_1100 | Load data stored in RAM (at the 10-bit address stored in Ry) to register Rx |  |  |  |  | 
STR Str *Rx, Ry | 00_XX_YY_1101 | Store the data from Ry into RAM at the 10-bit address stored in Rx |  |  |  |  | 

## Slide 14
Immediate Instructions
T00
T01
T 11
T 10
T00: 0th
- Enable Extern: get the instruction from the switches into the BUS
- Enable IR: store instruction in Instruction Register
T01: 0th
- Enable Extern: for reading the instruction into the BUS, then activate
- Enable Instruction Register: to read the instruction from the BUS, which now holds the extern instruction.
T00: 0th
-Enable Extern: for reading the instruction into the BUS, then activate
-Enable Instruction Register: to read the instruction from the BUS, which now holds the extern instruction.
T01: 0th
- Enable Extern: for reading the instruction into the BUS, then activate
- Enable Instruction Register: to read the instruction from the BUS, which now holds the extern instruction.
ADDI, SUBI
ADD Rx, Ry
00_XX_YY_0010

## Slide 15
Immediate Instructions
Function & Mnemonic | Opcode | Details | Procedure | T0=00 | T1=01 | T2=10 | T3=11
ADDI addi Rx, 6’bIIIIII | 10_XX_IIIIII | Add immediate value (IIIIII) to RX | Rx ← [[Rx]+ 10’b0000IIIIII] | Extrn = 1 enIR = 1 | Rout = Rx ENR = 1 Ain = 1 | IMM[5:0] = INST[5:0] IMM[9:6] = 4’b0000 ALUcont = 4b’0010 | Gout = 1 Rin = Rx enRin = 1 Clr = 1
SUBI subi Rx, 6’bIIIIII | 11_XX_IIIIII | Subtracts immediate value (IIIIII) from RX | Rx ← [[Rx] - 10’b0000IIIIII] |  |  | IMM[5:0] = INST[5:0] IMM[9:6] = 4’b0000 ALUcont = 4b’0010 | 

## Slide 16
RAM Instructions
01
10
00
T01: 1st
- Enable Extern: get instruction from the switches into the BUS
- Enable IR: store instruction in Instruction Register
T 10: 2nd
Enable Extern: for reading the instruction into the BUS, then activate
Enable Instruction Register: to read the instruction from the BUS, which now holds the extern instruction.
T00: 0th
-Enable Extern
-Enable Instruction Register
STR, LDR
ADD Rx, Ry
00_XX_YY_0010

## Slide 17
RAM Instructions
Function & Mnemonic | Opcode | Details | Procedure | T0=00 | T1=01 | T2=10 | T3=11
ADDI addi Rx, 6’bIIIIII | 10_XX_IIIIII | Add immediate value (IIIIII) to RX | Rx ← [[Rx]+ 10’b0000IIIIII] | Extrn = 1 enIR = 1 | Rout = Rx ENR = 1 Ain = 1 | IMM[5:0] = INST[5:0] IMM[9:6] = 4’b0000 ALUcont = 4b’0010 | Gout = 1 Rin = Rx enRin = 1 Clr = 1
SUBI subi Rx, 6’bIIIIII | 11_XX_IIIIII | Subtracts immediate value (IIIIII) from RX | Rx ← [[Rx] - 10’b0000IIIIII] |  |  | IMM[5:0] = INST[5:0] IMM[9:6] = 4’b0000 ALUcont = 4b’0010 | 

## Slide 18
Modules

## Slide 19
Debounces the peek and clock signals
Adds a tristate buffer to external input
Receives input from external sources
Splices data for the peek operation
Input Logic
INPUTS
Peek_key: Lets user view the registers
50MHZ: Internal clock of the DE10 Lite
RawCLK: Clock button
RawData: Data from the switches
Extrn_Enable: Lets data write to bus
OUTPUTS
PEEKb: Peek signal after debounced
CLKb: Clean clock signal after debounced
data2bit: To select register to peek
databus: Data to be written onto the bus
COMPONENTS
Debouncer: Cleans noisy signals

## Slide 20
Provides Timesteps for Controller
Synchronous clearing
Neg-edge triggered counting
Counter
INPUTS
CLR: clear signal to reset counter
CLKb: debounced clock signal
OUTPUTS
CNT: 2bit counter value of current count This is fed into the controller to help it keep track of the timesteps
COMPONENTS
Address Register: Saves memory address
1024x10: 10 bit Memory array

## Slide 21
Stores the Instruction during operation
Provides the instruction to the controller
Instruction Register
INPUTS
D: Data gotten from the bus
CLKb: Debounced clock (neg triggered)
EN: Enable signal to allow the register to save inputs
OUTPUTS
Q: Saved instruction to be sent to the controller
COMPONENTS
Register: Saves the actual data

## Slide 22
Data Storage
Reading & Writing
Intermediate Storage
Register File
INPUTS
D: Common 10-bit input data
ENW: Enable writing to registers
ENR0: Enables Q0 output write to bus
ENR1: Enables Q1 output
CLKb: Neg triggered clock for registers
WRA: Selects register to write to
RDA0: Selects register to read from
RDA1: Selects register to peek
OUTPUTS
Q0: Retrieved data from the register
Q1: Data from the peeked register
COMPONENTS
4 Registers: Saves 10bit data

## Slide 23
Provides a human Interface
Displays current data on the Bus
Lets users peek into register
Output Logic
INPUTS
BUS: Data from the shared bus
PEEKb: Input from user to peek
REG: Data peeked from register
TIME: Current timestep from counter
DONE: Clear signal from controller
COMPONENTS
Converter Function: converts data to hex
Mux function: Converts 4’b time to 7’b display
INPUTS
LED_B: Array of LEDs showing data on bus
DHEX#: 7 segment hex displays * 3
  Shows data on bus or register in peek
THEX: 7 seg display showing current timestep
LED D: shows that the operation is done

## Slide 24
Executes arithmetic perations
Stores data temporary in G register
Multi-stage ALU
INPUTS
CLKb: Clock for neg triggered registers
Ain: Enable for the A register
OP: Data from the shared bus
FN: Arithmetic instruction from controller
Gin: Enable write to G register
Gout: Enable read from G register
OUTPUTS
RES: Calculated result
COMPONENTS
A Register: Saves memory address
ALU: Performs calculations
G Register: Saves result from ALU

## Slide 25
Stores data from the registers
SDRAM
INPUTS
address: Memory address to be used
EN_Address: Lets Address Register read
CLKb: Negative edge triggered
EN_write: Allows write to ram
data_in: Data to be saved into RAM
EN_read: Allows bus to read from RAM
OUTPUTS
data_out: Data from ram to be sent back into the bus
COMPONENTS
Address Register: Saves memory address
1024x10: 10 bit Memory array

## Slide 26
Controller

## Slide 27
Managed Components
Register File
Get a modern PowerPoint Presentation that is beautifully designed.
Counter
Get a modern PowerPoint Presentation that is beautifully designed.
Shared Bus
- Allows data to be written to or read from the register file
- Picks which register to operate
Multi-stage ALU
- #####
SDRAM
- #####
Output Logic
-####
Input Logic
- #####
Instruction Register
- #####

## Slide 28
Controls the other modules in the processor.
Controller
INPUTS
INSTR: Instruction from instruction register
T: Timestep count from counter
COMPONENTS
Timestep Functions: Enables the output of the controller depending on timestep
OUTPUTS
Ext: Enables the external data input in the input logic
IRin: Enables the instruction register
Clr: Sends a reset signal to the counter, and a done signal to the output logic

## Slide 29
OUTPUTS
Controller
REGISTER FILE
#: ###
#: ###
#: ###
#: ###
REGISTER FILE
#: ###
#: ###
#: ###
#: ###

## Slide 30
How the Controller works
Nested if statements
If (T == 01)
if (INST == 0101)
#####
else if (INST == 0110)
#####
else if (T == 10)
if (INST == 0101)
#####
else if (INST == 0110)
#####
else if (T == 10)
if (INST == 0101)
#####
else if (INST == 0110)
#####
Default output disable
All outputs are disabled by default at the start of each timestep
Ensure only the things we want enabled are doing so.

## Slide 31
Shared Bus

## Slide 32
How the Bus works

## Slide 33
References
20%
20%
20%
20%
20%
You can simply impress your audience and add a unique zing and appeal to your Presentations.
You can simply impress your audience and add a unique zing and appeal to your Presentations.
You can simply impress your audience and add a unique zing and appeal to your Presentations.
You can simply impress your audience and add a unique zing and appeal to your Presentations.
You can simply impress your audience and add a unique zing and appeal to your Presentations.

## Slide 34
Tools used
Tracking commits and changes
GitHub Desktop
GIT GUI
GitHub Version control
Visual Studio Code
IDE
Git GUI for Desktop
Team collaboration
Syntax highlighting
Notion
Writing documentation
& info store
GitHub Copilot Questions and debugging
Compiling SV code Programing DE10
Compiling SV code Programing DE10
Lucid Chart
Designing diagrams

## Slide 35
Fall 2023, South Dakota State University
Thank
You!
John Akujobi - Amanuel Ayelew - Sukhmanjeetsingh LNU
BitBlaster 10bit Processor

## Slide 36
Comparison
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4 | Category 5 | Category 6
Series 1 | 45 | 50 | 65 | 50 | 35 | 75
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4 | Category 5 | Category 6
Series 1 | 65 | 55 | 40 | 80 | 40 | 20
Text
Content Here
Content
Your Content Here
Your Text Here
Text Here
75%
35%
50%
65%
50%
45%
65%
55%
40%
80%
40%
20%
You can simply impress your audience and add a unique zing and appeal to your Presentations. Easy to change colors, photos and Text.
Your Text Here
You can simply impress your audience and add a unique zing and appeal to your Presentations. Easy to change colors, photos and Text.
Your Text Here

## Slide 37
Infographic Style
Your Text
Name Here
Name Here
Name Here
Name Here
Name Here
Name Here
Name Here
Name Here
Name Here
Name Here
Name Here
Name Here
Name Here
Your Text
Name Here
Name Here
Name Here
Name Here
Name Here
Your Text
Name Here
Your Text
Name Here
CEO
Name Here
Your Text
Name Here

## Slide 38
Fully Editable Shapes